## Slide 1: Lecture 2: Edge detection
CS4186: Computer Vision
Prof. Zhu Zhiyu

## Slide 2: Edge detection
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAA
Convert a 2D image into a set of curves
  Extracts salient features of the scene
  More compact than pixels

## Slide 3: Origin of edges
Edges are caused by a variety of factors
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity

## Slide 4: Images as functions…
Edges look like steep cliffs

## Slide 5: Characterizing edges
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative
Source: L. Lazebnik

## Slide 6: Image gradient
The gradient points in the direction of most rapid increase in intensity
The gradient of an image:
The edge strength is given by the gradient magnitude:
The gradient direction is given by:
  how does this relate to the direction of the edge?
Source: Steve Seitz
Notes: give definition of partial derivative: lim h->0 [f(x+h,y) – f(x,y)]/h

## Slide 7: Image derivatives
How can we differentiate a digital image F[x,y]?
  Option 1: reconstruct a continuous image, f, then compute the derivative
  Option 2: take discrete derivative (finite difference)
1 | -1 | 
How would you implement this as a linear filter?
 | -1 | 
 | 1 | 
:
:
Source: S. Seitz

## Slide 8: Image gradient
Source: L. Lazebnik

## Slide 9: Effects of noise
Where is the edge?
Source: S. Seitz
Noisy input image
Notes: How to fix?

## Slide 10: Solution: smooth first
f
h
f * h
Source: S. Seitz
To find edges, look for peaks in

## Slide 11: Associative property of convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz

## Slide 12: The 1D Gaussian and its derivatives

## Slide 13: 2D edge detection filters
Gaussian
derivative of Gaussian (x)
Notes: How many 2nd derivative filters are there? There are four 2nd partial derivative filters.
In practice, it’s handy to define a single 2nd derivative filter—the Laplacian

## Slide 14: Derivative of Gaussian filter
x-direction
y-direction

## Slide 15: The Sobel operator
Common approximation of derivative of Gaussian
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
The standard definition of the Sobel operator omits the 1/8 term
    doesn’t make a difference for edge detection
    the 1/8 term is needed to get the right gradient magnitude
Notes: 15
Q: Why might these work better?
A: more stable when there is noise

## Slide 16: Sobel operator: example
Source: Wikipedia

## Slide 18: Example
original image
Demo: http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
Image credit: Joseph Redmon

## Slide 19
smoothed gradient magnitude
Finding edges

## Slide 20
thresholding
Finding edges
where is the edge?

## Slide 21: Get Orientation at Each Pixel
Get orientation (below, threshold at minimum gradient magnitude)
θ = atan2(gy, gx)
0
360
Gradient orientation angle

## Slide 22: Non-maximum supression
Check if pixel is local maximum along gradient direction
  requires interpolating pixels p and r

## Slide 23: Before Non-max Suppression

## Slide 24: After Non-max Suppression

## Slide 25
Thresholding edges
Still some noise
Only want strong edges
2 thresholds, 3 cases
  R > T: strong edge
  R < T but R > t: weak edge
  R < t: no edge
Why two thresholds?

## Slide 26
Connecting edges
Strong edges are edges!
Weak edges are edges iff they connect to strong
Look in some neighborhood (usually 8 closest)

## Slide 27: Canny edge detector
Filter image with derivative of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression
Linking and thresholding (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
Source: D. Lowe, L. Fei-Fei, J. Redmon
MATLAB: edge(image,‘canny’)

## Slide 28: Canny edge detector
Canny with
Canny with
original
The choice of depends on desired behavior
  large detects “large-scale” edges
  small detects fine edges
Source: S. Seitz

## Slide 29: Scale space [Witkin 83]
Properties of scale space (w/ Gaussian smoothing)
  edge position may shift with increasing scale ()
  two edges may merge with increasing scale
  an edge may not split into two with increasing scale
larger
Gaussian filtered signal
first derivative peaks

## Slide 30: Questions?